## Slide 1: mdtmFTP evaluation @ESNET Testbed
MDTM Research Team

## Slide 2: Goal
Test and evaluate mdtmFTP at WAN environment
Test and evaluate mdtmFTP at LXC-based VM environment
Compare mdtmFTP with other data transfer tools

## Slide 3: ESNET Testbed - 1
Data transfer:
DTN “nersc-tbn-2”  “nersc-tbn-1”.
95ms RTT loop between nersc-tbn-1 and nersc-tbn-2.
nersc-tbn-1
2xIntel HaswellXeon E5-2643 6 cores
Motherboard: superMicro X10DRi (PCIe Gen3)
2x40G Mellanox NICs
Support high performance I/O operation (Write)
  An array of 24 HDDs
nersc-tbn-2
2xIntel HaswellXeon E5-2643 6 cores
Motherboard: superMicro X10DRi (PCIe Gen3)
2x40G Mellanox NICs
Support high performance I/O operation (Read)
  An array of 12 SSDs

## Slide 4: ESNET Testbed - 2
ESNET Testbed supports PROXMOX-based Linux container (LXC) technology
  http://proxmox.com/
nersc-tbn-1 and nersc-tbn-2 each runs a Linux Container VM

## Slide 5: Evaluation Methodology - 1
Transfer data from nersc-tbn-2 to nersc-tbn-1
Performance metric: Time-to-Completion
Data transfer tool
  mdtmFTP (developed by FNAL)
    http://mdtm.fnal.gov
  FDT (developed by CalTech)
    http://monalisa.cern.ch/FDT/
  BBCP (developed by SLAC)
    https://www.slac.stanford.edu/~abh/bbcp/
  GridFTP (developed by University of Chicago)
    http://toolkit.globus.org/toolkit/docs/latest-stable/gridftp/

## Slide 6: Evaluation Methodology - 2
Transfer Mode
  Client-Server data transfer
  3rd-Party data transfer
Data Transfer Scenarios:
  Large file transfer: Transferring a 100GB large file from nersc-tbn-2 to nersc-tbn-1.
  Folder transfer 1: Transferring a folder that has 30 10G files from nersc-tbn-2 to nersc-tbn-1
  Folder transfer 2: Transferring a Linux-3.18.21 folder from nersc-tbn-2 to nersc-tbn-1

## Slide 7: Evaluation Methodology - 3
Data transfer tool configuration
Data Transfer tools | # of Parallel Streams | Pipelining | Currency | TCP parameters
FDT | 4 | N/A | N/A | System configuration
GridFTP | 4 | -PP | -CC 8 | System configuration
BBCP | 4 | N/A | N/A | System configuration
mdtmFTP | 4 | N/A | 2 I/O threads | System configuration
Note: when # of parallel streams > 4, data transfer performance has negligible changes

## Slide 8: Result – Client/Server
 | mdtmFTP | FDT | GridFTP | BBCP
Time-to-Completion (seconds) | 74.18 | 79.89 | 91.18 | Poor performance
Larger file data transfer – 1 x 100G (Smaller is better)
Folder data transfer – 30 x 10G (Smaller is better)
Folder data transfer – Linux 3.12.21 (Smaller is better)
 | mdtmFTP | FDT | GridFTP | BBCP
Time-to-Completion (seconds) | 192.19 | 217 | 320.17 | Poor performance
 | mdtmFTP | FDT | GridFTP | BBCP
Time-to-Completion (seconds) | 10.51 | DO NOT Work | 1006.02 | Poor performance
Note: BBCP performance is very poor, we do not list its results here

## Slide 9: Result – Client/Server
Chart: Relative performance improvement (base: GridFTP)
| mdtmFTP | FDT | GridFTP
 | 1.2292 | 1.1413 | 1
Large File Data Transfer (1x100G)
Folder Data Transfer (30x10G)
Chart: Relative performance improvement (base: GridFTP)
| mdtmFTP | FDT | GridFTP
 | 1.6659 | 1.4754 | 1
Chart: Relative performance improvement (Base: GridFTP)
| mdtmFTP | GridFTP
 | 95.72 | 1
Folder Data Transfer (Linux 3.12.21)
Note: Larger is better
Relative performance improvement (base: GridFTP) =
other tools’ Time-to-Completion
GridFTP’s Time-to-Completion

## Slide 10: Result – 3rd party data transfer
 | mdtmFTP | FDT | GridFTP | BBCP
Time-to-Completion (seconds) | 34.976 | N/A | 106.84 | N/A
Larger file data transfer – 1 x 100G (Smaller is better)
Folder data transfer – 30 x 10G (Smaller is better)
Folder data transfer – Linux 3.12.21 (Smaller is better)
 | mdtmFTP | FDT | GridFTP | BBCP
Time-to-Completion (seconds) | 95.61 | N/A | Do not work | N/A
 | mdtmFTP | FDT | GridFTP | BBCP
Time-to-Completion (seconds) | 9.68 | N/A | Do not work | N/A
Note: BBCP and FDT support 3rd party data transfer.
But BBCP and FDT can not run 3rd party data transfer on ESNET testbed due to testbed limitation

## Slide 11: Result – 3rd party data transfer
Chart: Relative performance improvement (Base: GridFTP)
| mdtmFTP | GridFTP
 | 3.054 | 1
Large File Data Transfer (1x100G)
Note: Larger is better
Relative performance improvement (base: GridFTP) =
other tools’ Time-to-Completion
GridFTP’s Time-to-Completion

## Slide 12: mdtmFTP status
Much stable now, but still has bugs
Need more time to improve the code, and package the software
  Only 1.0 FTE available
mdtmFTP is now evaluated and tested under controlled environments
  Work with ORNL to use mdtmFTP for KSTAR science data transfer
  Work with FNAL CMS to test and deploy mdtmFTP
  Work with ESNET to test and evaluate mdtmFTP on Linux Container-based VM

## Slide 13: mdtmFTP roadmap
FNAL officially started mdtmFTP development at Jan 2015.
  1.0 FTE
  reuse some basic Globus modules for rapid prototyping
    GridFTP protocol module, Globus xio module, Globus security model
We open a new software engineer position for mdtmFTP development
  We plan to replace mdtmFTP’s Globus modules

## Slide 14: Summary
Test and evaluate mdtmFTP at WAN environment
Test and evaluate mdtmFTP at LXC-based VM environment
Compare mdtmFTP with other data transfer tools
  Test results approve that we are in the right direction
mdtmFTP status
mdtmFTP roadmap